## Slide 1
Storage-Centric Systems for Genomics
and Metagenomics
Nika Mansouri Ghiasi
n.mansorighiasi@gmail.com

## Slide 2: Applications of Genomics and Metagenomics
Uncovering and treating diseases linked to genomic variations
Detecting pathogens in the environment
Rapid surveillance of disease outbreaks
Developing personalized medicine
Notes: Let's start by looking at some key applications in genome analysis.
[CLICK] For example, we can uncover, …
To enable many of these applications, we need to analyze the genomic data.

## Slide 3: DNA Under Electron Microscope

## Slide 4
CCTCCTCAGTGCCACCCAGCCCACTGGCAGCTCCCAAACAGGCTCTTATTAAAACACCCTGTTCCCTGCCCCTTGGAGTGAGGTGTCAAGGACCTAAACTAAAAAAAAAAAAAGAAAAAGAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTCATGTCAAGGACCTAATGTGCTAAACAGCACTTTTTTGACCATTATTTTGGATCTGAAAGAAATCAAGAATAAATGAAGGACTTGATACATTGGAAGAGGAGAGTCAAGGACCTACAGAAAAAAAAAAAAAAGAAAAAGAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTCATGTCAAGGACCTAATGTCTGTGTTGCAGGTCTTCTTGCATTTCCCTGTCAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTCATGTCAAGGACCTAATGTCAGGCC
GGCTCTTATTAAAACACCCTGTTCCCTGCCCCTTGGAGTG

## Slide 5: High-Throughput Sequencers
… and more! All produce data with different properties.
Illumina MiSeq
Oxford Nanopore MinION
Pacific Biosciences RS II
Illumina NovaSeq 6000
Oxford
Nanopore SmidgION
Pacific
Biosciences
Sequel II
Oxford
Nanopore
PromethION

## Slide 6: High-Throughput Sequencers
… and more! All produce data with different properties.
Illumina MiSeq
Oxford Nanopore MinION
Pacific Biosciences RS II
Illumina NovaSeq 6000
Oxford
Nanopore SmidgION
Pacific
Biosciences
Sequel II
Oxford
Nanopore
PromethION
Current sequencing technologies
cannot sequence very long DNA molecules end-to-end
Instead, they extract smaller fragments of the original DNA sequence, known as reads
AAGCTTCCATGG
AAATGGGCTTTC
GCCCAAATGGTT
GCTTCCAGAATG

## Slide 7: Genome Sequence Analysis
Read mapping: first key step in genome sequence analysis
…GCCCATATGGTTAAGCTTCCATGGAAATGGGCTTTCGCTTCCACAATG…
  Aligns reads to potential matching locations in the reference genome
Reference Genome
Differences
Differences
  For each matching location, the alignment step finds the degree of similarity (alignment score)
AAGCTTCCATGG
GCCCAAATGGTT
GCTTCCAGAATG
AAATGGGCTTTC
Calculating the alignment score requires computationally-expensive approximate string matching (ASM) to account for differences between reads and the reference genome due to:
  Sequencing errors
  Genetic variation
Notes: Read mapping is the first key step in genome sequence analysis [CLICK]
That Aligns reads to potential matching locations within the reference genome [CLICK]
For each matching location, the alignment step finds the degree of similarity between read and reference by calculating the alignment score
Calculating the alignment score requires computationally-expensive approximate string matching (ASM) to account for differences between reads and the reference genome. [CLICK]

## Slide 8: Genome Sequence Analysis
Computation overhead
Data movement overhead
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Alignment
Data Movement
Storage
System
Notes: Read mapping performs alignment on large genomic datasets, containing millions of reads. [CLICK]
Therefore, read mapping is both computationally expensive [CLICK]
And incurs high data movement overhead [CLICK]

## Slide 9: What is Metagenomics?
Metagenomics: Study of genome sequences of diverse organisms
within a shared environment (e.g., blood, ocean, soil)
Overcomes the limitations of traditional genomics
  Bypasses the need for analyzing individual species in isolation
Notes: Metagenomics: Study of genome sequences of diverse organisms within a shared environment (e.g., blood, ocean, soil)
Metagenomics overcomes the limitations of traditional genomics
Because it bypasses the need for culturing individual species in isolation,
which is not feasible in many important clinical and environmental use cases

## Slide 10: What is Metagenomics?
Has led to groundbreaking advances
Precision medicine
Understanding microbial diversity of an environment
Discovering early warnings of communicable diseases
Metagenomics: Study of genome sequences of diverse organisms
within a shared environment (e.g., blood, ocean, soil)
Notes: Therefore, metagenomics has led to ground-breaking advances
In many fields such as
Precision medicine
Understanding microbial diversity of an environment
Discovering early warnings of communicable diseases

## Slide 11: Metagenomic Analysis
A large database
containing information
on many species
Metagenomic sample
with species that
are not known in advance
Preparation
of Input Queries
Query
K-mers
…
GCTCA
CTCAT
TCATG
Presence/Absence Identification
Abundance
Estimation
V. cholerae
E. coli
SARS-CoV-2
Chart: 
| Species#1 | Species#2 | Species#3
 | 0.6 | 0.25 | 0.15
(e.g., > 100 TBs in emerging databases)
Notes: Since the species that are present in a metagenomic sample are not known in advance,
Metagenomic analysis performs tasks to enable an understanding of the sample’s composition.
Here, I am going to start with showing the genomic sequences of the organisms in the metagenomic sample,
To perform metagenomic analysis
First, many tools extract k-mers (i.e., subsequences of length k) from the input queries in a sample
Second, they find species present/absent in the sample by searching the query k-mers against a large metagenomic database containing information on many species’ genomes.
Many databases used for various use cases can be very large, for example, to several TBs or more than a hundred TBs in emerging databases
This step outputs the IDs of the species that are identified to be present in the sample
Finally, some applications perform a third optional step of abundance estimatimation,
which calculates the relative frequencies of the occurrence of different species in the sample

## Slide 12: Problems with (Meta) Genome Analysis Today
Special-Purpose Machine
for Data Generation
FAST
SLOW
General-Purpose Machine
for Data Analysis
Slow and inefficient processing capability
Large amounts of data movement

## Slide 13: Illumina DRAGEN Bio-IT Platform (2018)
Processes whole genome at 30x coverage in ~25 minutes with hardware support for data compression
FPGA board(s)
emea.illumina.com/products/by-type/informatics-products/dragen-bio-it-platform.html
emea.illumina.com/company/news-center/press-releases/2018/2349147.html

## Slide 14: NVIDIA Clara Parabricks (2020)
https://developer.nvidia.com/clara-parabricks
GPU board(s)
A University of Michigan startup in 2018 joined NVIDIA in 2020

## Slide 15: NVIDIA Hopper DPX Instructions (2022)
https://blogs.nvidia.com/blog/2022/03/22/nvidia-hopper-accelerates-dynamic-programming-using-dpx-instructions/

## Slide 16: Bionano & NVIDIA: Accelerating Analysis for Fast Time to Results
We are accelerating the transformation in how we analyze the human genome!
New high-performance algorithms from Bionano
Technological solution to support higher throughput
Powered by NVIDIA RTX™ 6000
Ada Generation GPUs
Workflow tailored for a small lab and
IT footprint
Notes: Partnership
Designed to scale from small labs that do not have datacenters to datacenters and cloud

## Slide 17: Accelerating Genome Sequence Analysis
Heuristics
Accelerators
Filters
Computation overhead
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
Storage
System
Data movement overhead
✓
Notes: There has been significant effort into improving read mapping performance [CLICK]
Through efficient heuristics [CLICK]
hardware accelerators [CLICK]
and various filters that prune reads that do not require expensive computation [CLICK].
While these approaches address the computation overhead in read mapping [CLICK]
[While Reads Move] None of them alleviate the data movement overhead from storage, whose impact becomes even larger when the computation overhead gets alleviated [CLICK]

## Slide 18: Storage-Centric Systems for (Meta)Genomics
Genomics
GenStore (ASPLOS’22)
Metagenomics
MegIS (ISCA’24)
Efficient Analysis on Compressed Genomic Data
SAGe (arXiv’25)
Emerging Areas in (Meta)Genomics
MARS (ICS’25) Raw Genomics Signal Analysis
GRAINS Genome Graph Analysis

## Slide 19: Storage-Centric Systems for (Meta)Genomics
Genomics
GenStore (ASPLOS’22)
Metagenomics
MegIS (ISCA’24)
Efficient Analysis on Compressed Genomic Data
SAGe (arXiv’25)
Emerging Areas in (Meta)Genomics
MARS (ICS’25) Raw Genomics Signal Analysis
GRAINS Genome Graph Analysis

## Slide 20: Key Idea
Storage
System
Non-matching reads
Do not have potential matching locations and can skip alignment
Filter reads that do not require alignment
inside the storage system
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Filtered Reads
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
Exactly-matching reads
Do not need expensive approximate string matching during alignment
Notes: Our key idea is to filter reads that do not require the expensive alignment computation in the storage system [CLICK] …
[While Reads Move] To fundamentally reduce the data movement overhead of read mapping
Examples of the reads that not require the costlt alignment step
Exactly-matching reads to the reference genome that do not need approximate string matching performed during alignment
Non-matching reads that have no potential matching locations in the reference genome hence skip the alignemt step

## Slide 21: Challenges
Read mapping workloads can exhibit different behavior
There are limited hardware resources
in the storage system
Filter reads that do not require alignment
inside the storage system
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Filtered Reads
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
Storage
System
Notes: However, filtering reads in a modern SSD can be challenging [CLICK]
Due to different behavior across read mapping workloads. [CLICK]
And the limited hardware resources in the SSD. By addressing these challenges [CLICK]

## Slide 22: GenStore
Computation overhead
Data movement overhead
  GenStore provides significant speedup (1.4x - 33.6x) and
  energy reduction (3.9x – 29.2x) at low cost
Filter reads that do not require alignment
inside the storage system
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
GenStore-Enabled
Storage
System
✓
✓
Notes: We propose GenStore, the first in-storage processing system designed for genome sequence analysis. [CLICK]
To reduce both the computation [CLICK]
And the data movement overhead [CLICK]
GenStore provides high-performance and energy benefits compared to state-of-the-art HW and SW baselines [CLICK]

## Slide 23: More in the Paper
https://arxiv.org/abs/2202.10400
https://github.com/CMU-SAFARI/GenStore
Notes: Let me briefly talk about other results that are included in the paper before concluding this talk. These include the following:

## Slide 24: Storage-Centric Systems for (Meta)Genomics
Genomics
GenStore (ASPLOS’22)
Metagenomics
MegIS (ISCA’24)
Efficient Analysis on Compressed Genomic Data
SAGe (arXiv’25)
Emerging Areas in (Meta)Genomics
MARS (ICS’25) Raw Genomics Signal Analysis
GRAINS Genome Graph Analysis

## Slide 25: Metagenomic Analysis
A large database
containing information
on many species
Metagenomic sample
with species that
are not known in advance
Preparation
of Input Queries
Query
K-mers
…
GCTCA
CTCAT
TCATG
Presence/Absence Identification
Abundance
Estimation
V. cholerae
E. coli
SARS-CoV-2
Chart: 
| Species#1 | Species#2 | Species#3
 | 0.6 | 0.25 | 0.15
(e.g., > 100 TBs in emerging databases)
Notes: Since the species that are present in a metagenomic sample are not known in advance,
Metagenomic analysis performs tasks to enable an understanding of the sample’s composition.
Here, I am going to start with showing the genomic sequences of the organisms in the metagenomic sample,
To perform metagenomic analysis
First, many tools extract k-mers (i.e., subsequences of length k) from the input queries in a sample
Second, they find species present/absent in the sample by searching the query k-mers against a large metagenomic database containing information on many species’ genomes.
Many databases used for various use cases can be very large, for example, to several TBs or more than a hundred TBs in emerging databases
This step outputs the IDs of the species that are identified to be present in the sample
Finally, some applications perform a third optional step of abundance estimatimation,
which calculates the relative frequencies of the occurrence of different species in the sample

## Slide 26: Motivation
Case study of the performance of metagenomic analysis tools
With various state-of-the-art SSD configurations
Normalized Throughput
Database Size (Terabyte)
I/O data movement causes significant performance overhead
Chart: 
| 0.7 | 1.4
No I/O | 1 | 1
Performance-Optimized | 0.31054 | 0.24299
Cost-Optimized | 0.03627 | 0.025496
3.2x
4.1x
27.6x
39.2x
Notes: We perform a case study on the throughput of metagenomic analysis tools
with various state-of-the-art cost-optimized or performance-optimized SSD configurations
And normalized throughput compared to a hypothetical configuration with zero performance overhead due to storage I/O
We observe that I/O data movement causes significant performance overhead

## Slide 27: Motivation
Case study on the throughput of metagenomic analysis tools
With Various state-of-the-art SSD configurations
Normalized Throughput
Database Size (Terabyte)
Chart: 
| 0.7 | 1.4
SSD-C | 0.03627 | 0.025496
SSD-P | 0.31054 | 0.24299
No-I/O | 1 | 1
I/O data movement causes significant performance overhead
Cost-Optimized
Performance-Optimized
No I/O
I/O becomes an even larger overhead (by 2.7x)
in systems where other bottlenecks are alleviated

## Slide 28: I/O Overhead is Hard to Avoid
I/O overhead due to accessing large, low-reuse data is hard to avoid
Sampling techniques to shrink database sizes
Keeping all data required by metagenomic analysis
completely and always resident in main memory
Reduce accuracy to levels unacceptable for many use cases
Energy inefficient, costly, unscalable, and unsustainable
Database sizes increase rapidly (doubling every few months)
Different analyses need different databases
[Wood+, Genome Biology’19], [Ounit+, BMC Genomics’15], [Kim+, Genome Research’16], …
Notes: I/O overhead from moving large, low-reuse data is hard to avoid
One might think it is possible to avoid this overhead by
using sampling techniques to shrink database sizes
However, this approach inevitably reduces accuracy to levels unacceptable for many use cases
Or another potential solution might seem to be
Keeping all data required by metagenomic analysis
completely and always resident in main memory
However, this is energy inefficient, costly, unscalable, and unsustainable due to two reasons
First, the sizes of metagenomic databases (which are already large, i.e., in some recent examples, exceeding a hundred terabytes) have been increasing rapidly.
For example, recent trends show the doubling of different important databases in only several months
Second, regardless of the sizes of individual databases, different analyses need different databases,
with information from different sets of genomes or with varying parameters.
Therefore, it is inefficient and unsustainable to maintain all data required by all possible analyses in main memory at all times

## Slide 29: Our Goal
Improve metagenomic analysis performance
by reducing large data movement overhead
from the storage system
in a cost-effective manner and with high accuracy
Notes: Motivated by these points, Our Goal is to Improve metagenomic analysis performance
by reducing the large data movement overhead from the storage system in a cost-effective manner

## Slide 30: Challenges of In-Storage Processing
No metagenomic analysis tools can run in-storage due to SSD limits
  Long latency of NAND flash chips
  Limited DRAM capacity inside the SSD
  Limited DRAM bandwidth inside the SSD
SSD DRAM
⋯
SSD
Controller
Cores
FTL
⋯
SSD
Cntrl
Cntrl
Channel#N
Channel#1
Notes: While In-Storage Processing (ISP) can be a promising direction to achieve our goal by processing data directly inside the storage device,
none of the existing approaches can be effectively implemented
as an ISP system due to limited hardware resources in the SSD such as
  Long latency of NAND flash chips
  Limited DRAM capacity inside the SSD
  And its limited bandwidth

## Slide 31: MegIS: Metagenomics In-Storage
First in-storage system for end-to-end metagenomic analysis
Idea: Cooperative in-storage processing for metagenomic analysis
  Hardware/software co-design between the storage system and host system
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
Notes: Which is the first in-storage processing system for end-to-end metagenomic analysis
The key idea of megis is Cooperative ISP for metagenomics
Which is enabled by a synergistic hardware/software co-design between the storage system and the host system

## Slide 32: MegIS Hardware-Software Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
Notes: To (i) leverage and (ii) orchestrate the capabilities of both systems, megis includes hw/sw co-design in 5 directions

## Slide 33: MegIS Hardware-Software Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
Step 1
Task partitioning and mapping
Each step executes
in its most suitable system
Step 2
Step 3

## Slide 34: MegIS Hardware-Software Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
Data/computation flow coordination
Reduce communication overhead
Reduce #writes to flash chips
Step 1
Step 2
Step 3
Task partitioning and mapping
Each step executes
in its most suitable system

## Slide 35: MegIS Hardware-Software Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
Cntrl
Cntrl
Channel#N
Channel#1
Storage-aware algorithms
Enable efficient
access patterns to the SSD
Step 1
Step 2
Step 3
Data/computation flow coordination
Reduce communication overhead
Reduce #writes to flash chips
Task partitioning and mapping
Each step executes
in its most suitable system

## Slide 36: MegIS Hardware-Software Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
ACC
ACC
Cntrl
Cntrl
Channel#N
Channel#1
Lightweight in-storage accelerators
Minimize SRAM/DRAM buffer spaces needed inside the SSD
Step 1
Step 2
Step 3
Storage-aware algorithms
Enable efficient
access patterns to the SSD
Data/computation flow coordination
Reduce communication overhead
Reduce #writes to flash chips
Task partitioning and mapping
Each step executes
in its most suitable system

## Slide 37: MegIS Hardware-Software Co-Design
Host System
SSD DRAM
Standard
Metadata
⋯
SSD
Controller
Cores
FTL
⋯
MegIS-Enabled SSD
MegIS
FTL
MegIS
Metadata
Cntrl
Cntrl
Channel#N
Channel#1
Data mapping scheme and Flash Translation Layer (FTL)
Specialize to the characteristics of metagenomic analysis
Leverage the SSD’s full internal bandwidth
Step 1
Step 2
Step 3
Storage-aware algorithms
Enable efficient
access patterns to the SSD
Lightweight in-storage accelerators
Minimize SRAM/DRAM buffer spaces needed inside the SSD
Data/computation flow coordination
Reduce communication overhead
Reduce #writes to flash chips
Task partitioning and mapping
Each step executes
in its most suitable system
ACC
ACC
Notes: 6 mins until here

## Slide 38: System Cost-Efficiency
Cost-optimized system ($): With SSD-C and 64-GB DRAM
Performance-optimized system ($$$): With SSD-P and 1-TB DRAM
GMean Speedup
Chart: 
| Perf-Opt ($) | Acc-Opt ($) | Perf-Opt($$$) | Acc-Opt ($$$) | MegIS ($)
 | 1 | 0.81324 | 6.8304 | 2.2454 | 16.1756
MegIS outperforms the baselines
even when running on a much less costly system
($)
($)
($$$)
($$$)
($)
7.2x
2.4x
16.2x
19.9x
Notes: Self-note (copy from arxiv version): For the performance-optimized system, we calculate the cost of 1TB
DRAM to be roughly 7080 USD (8 x 128GB modules [230]) and the cost of
SSD-P to be roughly 875 USD. For the performance-optimized system, we calculate
the cost of 64GB DRAM to be roughly 312 USD (8 x 8GB modules [231],
assuming the same number of memory channels as the performance-optimized
system) and the cost of SSD-C to be roughly 346 USD. Note that the cost of
the total storage system depends not only on the price of each SSD but also on
the available interconnection slots in the systems, as systems typically have
fewer PCIe slots (needed for SSD-P) than SATA slots (needed for SSD-C).

## Slide 39: More in the Paper
https://arxiv.org/abs/2406.19113
https://github.com/CMU-SAFARI/MegIS

## Slide 40: Storage-Centric Systems for (Meta)Genomics
Genomics
GenStore (ASPLOS’22)
Metagenomics
MegIS (ISCA’24)
Efficient Analysis on Compressed Genomic Data
SAGe (arXiv’25)
Emerging Areas in (Meta)Genomics
MARS (ICS’25) Raw Genomics Signal Analysis
GRAINS Genome Graph Analysis

## Slide 41: Large-Scale Genome Graphs
More powerful and efficient representations of genomic data
✓
Input Sequences
TATGACGAG
ATGA
TATG
TATGCCGAG
ATGC
TATG
TATGGCGAG
ATGG
TATG
…
…
…
TATGTCGAG
ATGT
TATG
…
TATG
ATGACGA
ATGCCGA
ATGGCGA
ATGTCGA
CGAG
Graph Representation
More compact representations of massive, population-scale databases
Greater expressive power
✓

## Slide 42: GRAINS
First in-storage processing system for large-scale genome graphs
More storage-friendly analysis via specialized execution flow and scheduling
Further improve performance, energy-efficiency, and cost-effectiveness via
via in-storage and in-flash processing
GRAINS provides significant speedup (1.5x – 47.8x) and
energy reduction (3.1x-31.6x) at low cost

## Slide 43: Raw Signal Genome Analysis (RSGA)
Raw Signals
CTGCGT...
Basecalling
Read Mapping
✓
Efficient analysis with better scalability and portability
✓
Raw signals contain richer information than bases
MARS: First In-Storage-Processing system for RSGA
  Targeted software modifications to optimize RSGA for in-storage executions
  Processing-In-Memory within the SSD to accelerate RSGA steps
MARS provides significant speedup (28x – 93x) and significant energy reduction at low cost

## Slide 44: Raw Signal Genome Analysis (RSGA)
Raw Signals
CTGCGT...
Basecalling
Read Mapping
✓
Efficient analysis with better scalability and portability
✓
Raw signals contain richer information than bases
MARS: First In-Storage-Processing system for RSGA
  Targeted software modifications to optimize RSGA for in-storage executions
  Processing-In-Memory within the SSD to accelerate RSGA steps
MARS provides significant speedup (28x – 93x) and significant energy reduction at low cost
https://arxiv.org/pdf/2506.10931

## Slide 45: Storage-Centric Systems for (Meta)Genomics
Genomics
GenStore (ASPLOS’22)
Metagenomics
MegIS (ISCA’24)
Efficient Analysis on Compressed Genomic Data
SAGe (arXiv’25)
Emerging Areas in (Meta)Genomics
MARS (ICS’25) Raw Genomics Signal Analysis
GRAINS Genome Graph Analysis

## Slide 46: Genomic Data is Growing at a Fast Pace
development of high-throughput sequencing (HTS) technologies
http://www.economist.com/news/21631808-so-much-genetic-data-so-many-uses-genes-unzipped
Number of Genomes Sequenced
Notes: The HTS technology is providing us with a lot of data because sequencing machines have become extremely high throughout and energy efficient
in a way that the genome analysis becomes much less costly faster than a transistor becomes much less costly with traditional Moore’s law curve. As a result we can sequence many genomes

## Slide 47: Genomic Data is Growing at a Fast Pace
development of high-throughput sequencing (HTS) technologies
http://www.economist.com/news/21631808-so-much-genetic-data-so-many-uses-genes-unzipped
Number of Genomes Sequenced
Accelerate genome sequence analysis
Store genome sequence data in highly-compressed formats
Data Preparation Bottleneck
Where genomic sequence data is stored in compressed form and needs to be decompressed and formatted first before an accelerator can operate on it
Notes: The HTS technology is providing us with a lot of data because sequencing machines have become extremely high throughout and energy efficient
in a way that the genome analysis becomes much less costly faster than a transistor becomes much less costly with traditional Moore’s law curve. As a result we can sequence many genomes

## Slide 48: Effect of Data Preparation Bottleneck
Prep
Analysis
Analysis
Analysis
Base.
Acc. Analysis
w/ Ideal Prep.
Prep
Prep
Lost Benefit due to Data Prep. Bottleneck
Execution Timeline
Acc. Analysis
Potential Benefit of Genome Analysis Acceleration
Baseline Analysis (446 KRead/s)
Accelerated Analysis (69200 KRead/s)
Baseline Prep. (2563 KRead/s)
Ideal Prep. (> 69200 KRead/s)

## Slide 49: SAGe
An algorithm-architecture co-design for highly-compressed storage and high-performance access of large-scale genomic sequence data
  Carefully exploits properties of genomic data in synergistically co-designing algorithms and hardware
✓
High compression ratios
Comparable to state-of-the-art genomic-specific compressors
✓
Fast decompression using only lightweight hardware and efficient streaming accesses
Can integrate with genomics systems even in resource-constrained environments
Portable systems
Near-data processing systems (e.g., in storage or memory)
SAGe improves the average end-to-end performance (3.0×–32.1×) and energy efficiency (13.0×–34.0×) of genome sequence analysis accelerators

## Slide 50: More in the Paper
https://arxiv.org/pdf/2504.03732

## Slide 51: Conclusion
Genomics
GenStore (ASPLOS’22)
Metagenomics
MegIS (ISCA’24)
Efficient Analysis on Compressed Genomic Data
SAGe (arXiv’25)
Emerging Areas in (Meta)Genomics
GRAINS Genome Graph Analysis
MARS (ICS’25) Raw Genomics Signal Analysis
Storage-Centric Systems for (Meta)Genomics

## Slide 52: Conclusion
Performance
Energy Efficiency
Cost Effectiveness
Robustness Security & Privacy
Make accurate (meta)genomic analysis more accessible for wider adoption
Storage-Centric Systems for (Meta)Genomics

## Slide 53: More About My Research
Near-Data Processing
(Other Works)
ALP IEEE TETC’22
SIMDRAM ASPLOS’21
CODIC ISCA’21
Venice ISCA’23
CAL MICRO’18
CROW ISCA’19
Optimizing Memory
and Storage Systems
FIGARO MICRO’20
FLIN ISCA’18
Algorithms
MLA ISMB’24
RawHash ISMB’23
BLEND NARGAB’23
TargetCall APBC’23
Algorithm-Architecture Co-Design
Scrooge Bioinformatics’23
SeGraM ISCA’22
SMASH MICRO’19
Device-Architecture Co-Design
Understanding and Modeling Ultra-Dense 3D Memory Systems PACT SRC’24
https://bit.ly/nikamgh
My Website:
Works Described in This Talk
MARS ICS’25
MegIS ISCA’24
GRAINS Ongoing
SAGe arXiv’25
REIS ISCA’25
IMPACT DSN’25
Ariadne HPCA’25
GenStore ASPLOS’22

## Slide 54
Storage-Centric Systems for Genomics
and Metagenomics
Nika Mansouri Ghiasi
n.mansorighiasi@gmail.com